## Slide 1: Distributed & Collaborative Monitoring in SDN
﻿An Equal Opportunity University

## Slide 2: Motivation
Traditional monitoring is sampling

## Slide 3: Motivation
Sampling is coarse-grained
  Sample rate is low
Sampling fails short in
  Application identification
  Anomaly detection
  More…

## Slide 4: Motivation
Per-flow monitoring

## Slide 5: Motivation
Per-flow monitoring
  Rule-based
    Large memory space
  Aggregation-based
    False positive
    Non-trivial memory space
Match | MonAct
f1 | Sample
f2 | Count
Match | MonAct
10.0.0.0/24 | Sample
10.0.0.1/24 | Count

## Slide 6: Distributed & Collaborative Monitoring
  Each flow may have its own action requirements.
  Millions of flows
Task:
  Distribute actions among switches.
  Represent rules compactly
Notes: In a typical network, there may be millions of flows, each of the flows may have its own monitoring action requirement,
So the task of DCM is to distribute the monitor actions among the switches, so that each of the switches is responsible for a certain number of monitoring tasks on a set of flows and work collarboratively.,and , we need to Represent the monitoring rules effiencetly.

## Slide 7: Approach: Bloom Filters
Use Bloom Filters to identify flows that should be monitored.
Populated by central controller.
Bloom Filter {f1,f3,f5} Counting
Bloom Filter {f1}  Sampling
Notes: Our approach to provide such memory effienciy ,is to use bloom filters to represent the set of flows that should be monitored by a certain monitoring action.
For example, there are two bmfs installed on this switch, here we let packets of flow f1,f3,f5 goes to heavy hitter detection, and do sampling on flow f1.

## Slide 8: DCM Data Plane: Two-stage Bloom Filters
No Monitoring Action
Admission
Bloom Filter
Notes: For the dataplane of the switch, DCM uses TWO-stage bloom filters to decide which monitoring actions it should carry out.
On Recving a packet, DCM will check the packet using the Adm bloom filter. It selectes the packets that belongs to the flows monitored on this switch. Usually, the majority of the packets will not pass it. Because only a small number of flows is monitored on one single switch. However, the adm bf does not specify which action should be taken on this packet.

## Slide 9: DCM Data Plane: Two-stage Bloom Filters
No Monitoring Action
BF
2
:
{
f
2
,
f
3
,
…
}
BF
3
:
{
f
4
,
f
5
,
…
}
…
..
BF
1
:
{
f
1
,
f
2
,
…
}
Action Bloom Filters
Match
Admission
Bloom Filter
Actions
...
ActA
ActB
ActC
Match
Notes: If a packet passes the adm blm filter , then it will be further checked by the action bloom filters to decide the corresponding monitor actions.
Each of the action bfs represents the set of flows that the specific action should be taken on.
If a packet passes a action bf, the corresponding actions will be taken on this packet.

## Slide 10: DCM Overview
controller
New flow notification
Packet miss

## Slide 11: Challenges
Flow dynamics
  Deletion
False positive in Data Plane
  Inaccurate monitoring
Task allocation
  Load balance, minimize FP

## Slide 12: Flow dynamics
Use CBF in Control Plane
  Support addition/deletion
  save space multiple times on switches
CBF in Control Plane
BF in Data Plane
Deletion

## Slide 13: False positive
Detect FP in Control Plane
  Simulate the behavior for new flows
  Mitigate FP in report
admBF
actBF1
actBF2
admBF
actBF1
actBF2
admBF
actBF1
actBF2
admBF
actBF1
actBF2
Match! FP!
No Match
No FP

## Slide 14: Task allocations
Minimize FP

## Slide 15: Task allocations
Minimize FP

## Slide 16: Task allocations
Minimize FP

## Slide 17: Task allocations
Minimize FP
Intuition: minimize 1s

## Slide 18: Task allocations
Is it practical to get minimum number of 1s?
It is NP-hard. (SetCover)

## Slide 19: Task allocations (Heuristics)
1
0
0
1
0
0
0
0
One more 1
Two more 1s
Starting from high-volume flows

## Slide 20: Task allocations (Heuristics)
Case 1:
  Exist complete overlapping.
  Choose the overlapping one.
Case 2:
  No complete overlapping.
  Consider both overlapping and workload.

## Slide 21: Task allocations
Real-time online allocation
Periodically offline refinement
Overloading handler

## Slide 22: Evaluation
Prototype emulation
  Click
Trace-driven simulation
  Real topologies + real traces

## Slide 23: Prototype emulation (single sw)
Overall false positive
PF of admBF

## Slide 24: Simulation (network wide)
Optimal range

## Slide 25: Simulation (Load balance)

## Slide 26: Case Study: Flow Size Counting with Count-Min Sketch
The overestimate ratio reduces significantly.
Notes: there are two case studies provided in our paper, here we show DCM helps to improve the memory efficiency for couting the flow size using count minium sktch.
Here the x axis indicates the size of total memory used (by the monitor rule table or blfms and the sketch,) the y axis indicates the overestimation under a certain memory limit.
Compared to the other two naïve approaches for per-flow monitoring, (monitor-all where the packets are monitored by all the switches on its path, and aggregation, where the flows are aggregated so that the total number of monitoring rules does not blow up.)
We can see that, when provided the same size of memory space, DCM reduces the overestimate ratio significantly.

## Slide 27
Thank you!
Notes: Thank you.